## Slide 1
Front panel
top
bottom
CCM_0010 revC Floating H-bridge + analog isolator
CCM_0008 revB FET driver
CCM_0008 revB FET driver
CCM_0010 revC Floating H-bridge + analog isolator
CCM_0008 revB FET driver
Q0 temp
Q0
external
INTERLOCK(S)
Top bypass control signal
Bottom bypass control signal
Notes:
All 3 CCM_0008 FET drivers are lab ground referenced, which is possible by using galvanically isolated CASR current sensors
Anti-parallel FET pairs above h-bridge stages use the FET body diodes to provide (a) kickback protection and (b) biasing for bypass stages
Current can be monitored directly by measuring across the sense resistor at bottom of chain
CaF MOT coils + cabling are ~0.1 ohms (1V ~ 10A)
At 10A DC, Q0 dissipates ~80W (12V supply = 8V*10A)
Top bypass setpoint (FP)
Top bypass monitor (FP)
Top h-bridge direction control (FP)
Bottom bypass monitor (FP)
Bottom h-bridge direction control (FP)
Bottom bypass setpoint (FP)
Current monitor (FP)
Current control setpoint (FP)
Simplified schematic for MOT coil control
12V
125A
0.01 ohms
100 W